Instruction Manual

LIFT & TILT TABLE

Note: Owner/Operator must read and understand this instruction

manual before using the lift & tilt table.

Thank you very much for selecting our LIFT & TILT TABLE. This instruction manual describes correct operating method to ensure prolonged service life. Please read and completely understand this manual before operating the LIFT & TILT TABLE. Always keep this manual at an appropriate place. If the manual or warning decal is missing, please contact with our dealer.

1.

WARNING!  If operating the lift & tilt table improperly, a person may be seriously injured. Therefore, operate properly according to the following instructions.

- Do not put foot or hand in scissors mechanism.

- Do not allow other people to stand in front of or behind the lift  & tilt table when it is moving.

- Do not move lift & tilt table when the table is at lifting position. Otherwise, load could fall down.

- Do not enter under the lift & tilt table.

- Do not overload the lift & tilt table.

- Do not put foot in front of rolling wheels. Otherwise, injury could result.

- Watch difference of floor lever when moving the lift & tilt table. Load could fall down.

- Do not use the lift & tilt table on a sloping or soft ground. Otherwise, the lift & tilt table may become uncontrollable and create danger.

- Do not lift people. Otherwise, people could fall down and suffer severe injury.

2.

CAUTION!   If operating the lift & tilt table improperly, a person may be injured. Therefore, operate properly according to the following instructions.

- Read this instruction manual carefully and completely understand how to operate the lift & tilt table.

- The lift & tilt table is a movable lifter designed to lift or lower rated load on the table. Do not use it for other purpose than its intended use.

- Do not allow a person to operate the lift & tilt table, who does not understand its operation.

- Do not lower the table too fast. Otherwise, load could fall down to create danger.

- Keep watching the condition of load. Stop operating the lift & tilt table right if load becomes unstable.

- Before lifting or lowering the table, make sure to brake the lift table.

- Ensure the balance of loading. Do not side or end load on the table. Load must be distributed on at least 80% of table area.

- Practice maintenance work according to service instructions.

- Do not modify the lift & tilt table without manufacturer’s written consent.

- Remove load from the table and use safety rod (Part No. 98) to prevent the table lowering when servicing the lift table.

- The lift & tilt table is not designed to be waterproof. Use the lift table under dry condition.

- Store the lift & tilt table indoor, and keep away from rain, water, or acid.

3. Name of parts

4. daily inspection

Before operating, please check the lift & tilt table according to the following points.

CAUTION!  Do not use the lift & tilt table if any malfunction or fault is found.

- Check if there is any scratch, bending or cracking on the lift & tilt table.

- Check if there is any hydraulic oil leakage from the hydraulic unit.

- Check if there is abnormal vertical creep of the table.

- Check the smooth movement of the wheels.

- Check the function of the brakes.

- Check if all the bolts and nuts are firmly tightened.

5. operatiON

  - How to Use the Brake

CAUTION!  Brake the lift & tilt table when not moving it in order to avoid sudden movement.

The brake is equipped with the swivel caster on the right side.

- Brake the wheel, press the brake pedal.

- Releasing the brake, lift up the brake pedal.

(Refer to the following figure.)

  - Lifting the Table

Warning!  Do not overload the lift & tilt table.

Ensure the balance of loading. Do not side or end load on the table. Load must be contributed on at least 80% of table area.

As the table is lifting, load will incline forward continuously.

When the table is lifted high, make sure that load should not move or fall off.

The hydraulic unit is designed to hold the table. The table should not stay at a lifting position for a long time.

- Press the lifting pedal several times until the table reaches any desired position.

- The table does not elevate after reaching the highest position even though the lifting pedal is pressed.

- The table lowers slightly after reaching the highest position.

  - Lowering the Table

Warning!  Do not put foot or hand in scissors mechanism.

- To lower the table, pull the lowering lever up.

6. Specifications

| Model | Capacity (kg) | Table | L x W x H (mm x mmx mm) | To-and-fro Lifting Times | Diameter of Wheel (mm) | Net Weight (kg) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Table Size (mm x mm) | Front (mm) | Rear (mm) |  |  |  |  |
| BL40 | 400 | 520 x 830 | 435 | 990 | 1355 x 520 x 1550 | 50 | 150 | 155 |
|  |  |  | 438 | 1560 |  |  |  |  |
| BL80 | 800 | 520 x 830 | 440 | 1000 | 1355 x 520 x 1550 | 68 | 150 | 172 |
|  |  |  | 438 | 1575 |  |  |  |  |

7. service INSTRUCTIONs

  - Lubricate each point described below every month.

  - Change hydraulic oil every year.

Lubricating Points

- Fitting of Cylinder …… Oil

- Roller Friction Surface …… Grease

- Link Pin …… Oil

- Pedal Fitting Point …… Oil

- Link Centre Pin …… Oil

- Joint …… Grease

- Grease Nipple …… Grease

8. HYDRAULIC CIRCUIT

9. PARTS LIST & EXPOLDED FIGURE

| Item No. | Description | Remark |
| --- | --- | --- |
| 1 | Seal Cover |  |
| 2 | Cylinder Cover |  |
| 3 | O-ring φ63x2.65 |  |
| 4 | Piston Rod |  |
| 5 | Piston |  |
| 6 | Y-ring |  |
| 7 | Retainer for Piston Rod |  |
| 8 | Spacing Retainer 18 |  |
| 9 | Spacing Casing |  |
| 10 | Cylinder |  |
| 11 | Washer for Cylinder |  |
| 12 | Reservoir |  |
| 13 | O-ring φ10x2.65 |  |
| 14 | Screw |  |
| 15 | Washer for Reservoir |  |
| 16 | Steel Ball |  |
| 17 | O-ring φ15x2.65 |  |
| 18 | Spring Base |  |
| 19 | Regulating Slide-valve |  |
| 20 | Regulating Pressure Spring |  |
| 21 | Regulating Speed Spring |  |
| 22 | O-ring φ8x1.8 |  |
| 23 | Regulating Pressure Screw |  |
| 24 | End Cover |  |
| 25 | Regulating Speed Slide-casing |  |
| 26 | Check Valve Screw |  |
| 27 | Check Valve Casing |  |
| 28 | O-ring φ6.9x1.8 |  |
| 29 | Steel Ball 7 |  |
| 30 | Conical Valve |  |
| 31 | Spring |  |
| 32 | O-ring φ10x1.8 |  |
| 33 | Lever |  |
| 34 | Lever Bushing |  |
| 35 | Washer 6 |  |
| 36 | Spring Washer 6 |  |
| 37 | Hexagonal Socket Screw M6x16 |  |
| 38 | O-ring φ10.6x2.65 |  |
| 39 | Guiding Casing |  |
| 40 | Spring |  |
| 41 | Reflux Rod |  |
| 42 | O-ring φ4x1.8 |  |
| 43 | Protect Casing |  |
| 44 | Pump Body |  |
| 45 | Pump Body for Plunger |  |
| 46 | Y-ring |  |
| 47 | Pump Plunger |  |
| 48 | Sealing Cover d18xD30 x7 |  |
| 49 | Spring |  |
| 50 | Spring Base |  |
| 51 | Handle |  |
| 52 | Panel |  |
| 53 | Nut |  |
| 54 | Steel Wire |  |
| 55 | Tube for Steel Wire |  |
| 56 | Spacing Casing |  |
| 57 | Spring Washer 12 |  |
| 58 | Hexagonal Socket Screw M12x40 |  |
| 59 | Pin Axle |  |
| 60 | Washer 8 |  |
| 61 | Split Pin |  |
| 62 | U Fork |  |
| 63 | Washer 8 |  |
| 64 | Spring Washer 8 |  |
| 65 | Screw |  |
| 66 | Pedal Bent Pipe |  |
| 67 | Bolt |  |
| 68 | Shake Link |  |
| 66 | Spring |  |
| 70 | Retaining Ring for Axle 10 |  |
| 71 | Pin Axle |  |
| 72 | Link |  |
| 73 | Hexagonal Socket Screw M10 |  |
| 74 | Washer 10 |  |
| 75 | Spring Washer 10 |  |
| 76 | Nut M10 |  |
| 77 | Frame of Rear Wheel |  |
| 77A | Frame of Front Wheel |  |
| 78 | Nut M12 |  |
| 79 | Washer 12 |  |
| 80 | Spacing Casing |  |
| 81 | Wheel |  |
| 82 | Bolt |  |
| 83 | Pin Axle |  |
| 84 | Retaining Ring for Axle 20 |  |
| 85 | Chassis |  |
| 86 | Screw M8x12 |  |
| 87 | Pin Axle |  |
| 88 | Slotting Nut M16x1.5 |  |
| 89 | Washer |  |
| 90 | Splitting Pin |  |
| 91 | Pin Axle |  |
| 92 | Bushing |  |
| 93 | Bushing |  |
| 94 | Internal Scissors Lever for Table |  |
| 95 | Nut M6 |  |
| 96 | Screw M8x12 |  |
| 97 | Internal Scissors Lever for Table |  |
| 98 | Scissors Lever |  |
| 99 | Spring Washer 6 |  |
| 100 | Table |  |
| 101 | Roller for Table |  |
| 102 | Bushing |  |
| 103 | Retaining Ring for Axle 18 |  |
| 104 | Safety Rod |  |
| 105 | Pin 8x14 |  |
| 106 | Nut M10 |  |
| 107 | Bolt M10x40 |  |
| 108 | Internal Scissors Lever for Chassis |  |
| 109 | External Scissors Lever for Chassis |  |
| 110 | Table |  |
| 111 | Pin Axle |  |
| 112 | Assembly of Guard |  |
| 113 | Washer 6 |  |
| 114 | Bolt M6x20 | Mechanical Strength Grade 8.8 |
| A | Piston Assembly |  |
| B | Pump Base Assembly |  |
| C | Pump Piston Assembly |  |
| D | Handle Assembly |  |
| E | Pedal Assembly |  |
| F | Swivel Wheel Assembly |  |
| G | Front Wheel Assembly |  |
| H | Pump Assembly |  |
| I | Seal Kit Assembly 1,3,6,13,17,22,28,32,38,46,48 |  |