#### Instruction Manual

#### BS Series

Note: Owner/Operator must read and understand this instruction manual             before using the lift table.

## Operation and Service Manual

BEFORE OPERATING THE LIFT TABLE, READ THIS MANUAL CAREFULLY AND UNDERSTAND COMPLETELY. KEEP THIS MANUAL ON FILE FOR FUTURE REFERENCE. IF THIS IS LOST, PLEASE CONTACT YOUR LOCAL SUPPLIER FOR A NEW COPY. ALSO, IF THE WARNING/CAUTION DECAL ON THE UNIT IS LOST, PLEASE CONTACT YOUR LOCAL SUPPLIER FOR A NEW DECAL.

NOTE: On this manual, WARNING means the danger which can lead to death or serious injury. CAUTION means the danger which can lead to slight injury or property damage.

- WARNING

1.DO NOT put foot or hand in scissors mechanism.

2.DO NOT allow other person to stand in front of or behind lift table when it is moving.

3.DO NOT move lift table when table is in raised position. Load could fall down.

4.DO NOT enter under table.

5.DO NOT overload lift table.

6.DO NOT put foot in front of rolling wheels. Injury could result.

7.WATCH difference and hardness of floor level when moving lift table. Load could fall down.

8.DO NOT use lift table on slope or inclined surface, lift table may become uncontrollable and create danger.

9.DO NOT lift people. People could fall down and suffer severe injury.

- CAUTION

1.Read this operation manual carefully and understand completely operating lift table. Improper operation could create danger.

2.This lift table is a movable lifter designed to lift or lower rated load on table. NO NOT use lift table for other purpose than its intended use.

3.DO NOT allow person to operate lift table who does not understand its operation.

4.DO NOT lower table too fast. Load could fall down and create danger.

5.KEEP watching the condition of load. Stop operating lift table if load becomes unstable.

6.Byake lift table when sliding load on of off table.

7.DO NOT side or end load. Load must be distributed on at least 80%of table area.

8.DO NOT use lift table with unstable, unbalanced loosely stacked load.

9.Practice maintenance work according to service instructions.

10. DO NOT modify lift table without manufacturer’s written consent.

11. REMOVE load from table and use safety stopper to prevent table from lowering when servicing lift table.

12. This lift table is not designed to be water resistant. Use lift table under dry condition.

- DAILY INSPECTION

Daily inspection is effective to find the malfunction or fault on lift table. Check lift table on the following points before operation.

CAUTION

DO NOT use lift table if any malfunction or fault is found.

- Check for scratch, bending or cracking on the lift table.

- Check if there is any oil leakage from the cylinder.

- Check the vertical creep of the table.

- Check the smooth movement of the wheel.

- Check the function of brake.

- Check if all the bolt and nuts are tightened firmly.

- OPERATING LIFTTABLE

4-1. How to use the brake.

CAUTION

Brake lift table when not moving it in order to prevent sudden movement.

The brake is equipped with the swivel caster on the right side.

- Braking the wheel, press the brake pedal.

- Releasing the brake, lift up the brake pedal.

4-2 Lifting the table

WARNING

DO NOT overload lift table, stay within its rated capacity. DO NOT side end load must be distributed on at least 80% of table area.

Press the lifting pedal several times the until the table reaches the desired position.

The table does not elevate after reaching the highest position even if the lifting pedal is pressed.

The table lowers slightly after reaching the highest position.

| MAXIMUM CAPACITY OF TABLE |
| --- |
| BS15 | BS25 | BS50 | BS75 | BS100 | BS30D | BS50D | BS80D |
| 150KG | 250KG | 500KG | 750KG | 1000KG | 300KG | 500KG | 800KG |

NOTE: The hydraulic cylinder is designed to hold table. As is the nature of the hydraulic system, table lowers very slowly over and extended period of time, Please note the table does not stay at the same position ionindefiinitely.

4-3. Lowering table

WARNING

DO NOT put foot or hand in scissors mechanism.

Pull the lowering down and table lowers.

- Specifications

| Model | Capacity (kg) | Table (mm) | Table Height(mm) | Stroke | L×W×H (mm) | Pedal to top. (approx. times) | Wheel (mm) φ | Weight (kg) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| BS15 | 150 | 700×450 | 225-760 | 535 | 1000×450×950 | 16 | 100 | 41 |
| BS25 | 250 | 830×500 | 335-915 | 580 | 1100×500×1010 | 25 | 125 | 78 |
| BS50 | 500 | 1010×520 | 430-1000 | 570 | 1130×520×1185 | 44 | 150 | 118 |
| BS75 | 750 | 1010×520 | 432-1000 | 568 | 1130×520×1260 | 55 | 150 | 120 |
| BS100 | 1000 | 1010×520 | 440-960 | 520 | 1130×520×1260 | 68 | 150 | 137 |
| BS30D | 300 | 1010×520 | 435-1585 | 1150 | 1130×520×1260 | 53 | 150 | 150 |
| BS50D | 500 | 1010×520 | 435-1585 | 1150 | 1130×520×1260 | 68 | 150 | 168 |
| BS80D | 800 | 1010×520 | 490-1400 | 910 | 1130×520×1275 | 95 | 150 | 165 |

- Service instruction

6.1-1. Lubricate each point described below every month:

6.2.Change hydraulic oil every 12 months.

Lubricating Points

- Fitting of cylinder……Oil

- Roller friction surface……Grease

- Link Pin ……Oil

- Pedal fitting point……Oil

- Link center pin……Oil

- Joint……Grease

- Grease nipple……Grease

- Hydraulic circuit

- Hydraulic Circuit

ASSEMBLY LIST

| DESCRIPTION | Quantity | PARTS ILLUST BEING INCLUDED |
| --- | --- | --- |
| Cylinder Assembly | 1 | 13-21 |
| Pump Unit Assembly | 1 | 64-78 |
| Pump Unit Sub Assembly | 1 | 22-58 |
| Handle Assembly | 1 | 84-91 |
| Pedal Assembly | 1 | 76-77 |

### PARTS LIST

| Item | Description | Qty. | Item | Description | Qty. |
| --- | --- | --- | --- | --- | --- |
| 1. | Table pair | 1 | 22. | Flow control joint | 1 |
| 2. | Guide roller | 4 | 23. | O ring | 1 |
| 3. | Scissors | 1 | 24. | Adjust casing | 1 |
| 4. | Snap ring | 6 | 25. | Spring seat | 1 |
| 5. | Link pin | 4 | 26. | Valve spring | 1 |
| 6. | Safety pin | 1 | 27. | Conical valve | 1 |
| 7. | Hex bolt | 16 | 28. | Valve seat | 1 |
| 8. | Washer | 18 | 29. | O ring | 1 |
| 9. | Frame pair | 1 | 30. | Busing | 1 |
| 10. | Front wheel | 2 | 31. | Dust seal | 1 |
| 11. | Spring washer | 19 | 32. | Y ring | 1 |
| 12. | Hex. nut | 18 | 33. | Plunger | 1 |
| 13. | Piston rod | 1 | 34. | Pump spring B | 1 |
| 14. | Dust seal | 1 | 35. | Pump spring A | 1 |
| 15. | O ring | 2 | 36. | Pump bass | 1 |
| 16. | Back up ring | 1 | 37. | Net | 1 |
| 17. | Cylinder pair | 1 | 38. | Washer | 1 |
| 18. | Spring seat | 1 | 39. | Back valve spring | 1 |
| 19. | Spring | 1 | 40. | O-ring | 1 |
| 20. | Seal ring | 1 | 41. | Plug | 1 |
| 21. | Joint | 1 | 42. | O ring | 1 |
| Item | Description | Qty. | Item | Description | Qty. |
| 43. | Steering bush | 1 | 67. | Pressure roller pin | 1 |
| 44. | O ring | 1 | 68. | Pedal Pivot Pin | 1 |
| 45. | Discharge lever | 1 | 69. | Hex. bolt | 2 |
| 46. | Valve arm | 1 | 70. | Elbow | 2 |
| 47. | Socket head screw | 1 | 71. | Oil return hose | 1 |
| 48. | Spring washer | 1 | 72. | Rubber bushing | 1 |
| 49. | Washer | 1 | 73. | High pressure hose | 1 |
| 50. | Bushing | 1 | 74. | Seal ring | 6 |
| 51. | Steel ball | 1 | 75. | Adaptor | 2 |
| 52. | Steel ball holder | 1 | 76. | Pedal Pair | 1 |
| 53. | Relief spring | 1 | 77. | Pedal rubber | 2 |
| 54. | Regulating pressure plug | 1 | 78. | Hex bolt | 1 |
| 55. | O ring | 1 | 79. | Lock bar | 1 |
| 56. | Relief plug | 1 | 80. | Hex. bolt | 1 |
| 57. | O ring | 1 | 81. | Cylinder pivot pin | 1 |
| 58. | Plug | 1 | 82. | Grease fitting | 2 |
| 59. | Rear wheel | 2 | 83. | Piston head pin | 1 |
| 60. | Handle pin | 4 | 84. | Roller chain | 1 |
| 61. | Handle lock spring L | 1 | 85. | Valve rod Ⅱ | 1 |
| 61A. | Handle lock spring R | 1 | 86. | Nut M6 | 1 |
| 62. | Bushing | 2 | 87. | Handle pair | 1 |
| 63. | Snap ring | 4 | 88. | Valve rodⅠ | 1 |
| 64. | Pedal holder | 1 | 89. | Control link | 1 |
| 65. | Snap ring | 2 | 90 | Roll pin | 1 |
| 66. | Pressure roller | 1 | 91. | Roll pin | 1 |

BS25

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover d30×D42×7 | 1 | 56. | Hex soch screw M6×16 | 1 |
| 2. | Cylinder cover | 1 | 57. | Tube for steel wire | 1 |
| 3. | O-ring d63×2.65 | 2 | 58. | Steel wire | 1 |
| 4. | O-ring d30×3.55 | 1 | 59. | Nut M8 | 24 |
| 5. | Piston rod | 1 | 60. | Washer 8 | 36 |
| 6. | Spacing casing | 1 | 61. | Spring pin | 1 |
| 7. | Guide ringδ1.5×15 | 1 | 62. | Spring pin | 1 |
| 8. | O-ring D20×2.4 | 1 | 63. | Control link | 1 |
| 9. | Seal ring d34×D40×4.5 | 1 | 64. | Handle | 1 |
| 10. | Piston rod retainer | 1 | 65. | Spacing casing | 2 |
| 11. | Retaining ring | 6 | 66. | Spring washer 12 | 2 |
| 12. | Piston | 1 | 67. | Hexagon head stud M12×40 | 2 |
| 13. | Cylinder | 1 | 68. | Split pin | 1 |
| 14. | Cylinder washer | 1 | 69. | Pin | 1 |
| 15. | Reservior | 1 | 70. | U-fork | 1 |
| 16. | O-ring d10×2.65 | 1 | 71. | Nut M6 | 1 |
| 17. | Filler screw | 1 | 72. | Bolt | 1 |
| 18. | Washer for reservior | 1 | 73. | Pedal bent pipe | 1 |
| 19. | Steel ball 5 | 1 | 74. | Pedal rubber | 1 |
| 20. | Spring base | 1 | 75. | Shake link | 1 |
| 21. | Regulating pressure spring | 1 | 76. | Spring washer 8 | 17 |
| 22. | Regulating pressure screw | 1 | 77. | Hex soch screw | 1 |
| 23. | O-ring d7.1×1.8 | 1 | 78. | Buffer mat | 1 |
| 24. | End cover | 1 | 79. | Partition set | 1 |
| 25. | O-ring d15×2.65 | 2 | 80. | Pin axle | 1 |
| 26. | Regulating speed spring | 1 | 81. | Retainer 10 | 2 |
| 27. | Regulating speed slide valve | 1 | 82. | Pin axle | 1 |
| 28. | Regulating speed spring casing | 1 | 83. | Retainer 20 | 1 |
| 29. | Regulating speed valve casing | 1 | 84. | Washer | 1 |
| 30. | Steel ball 7 | 1 | 85. | Pin axle | 1 |
| 31. | O-ring d6.9×1.8 | 1 | 86. | Link | 2 |
| 32. | Conical valve | 1 | 87. | Hex soch screw M8×20 | 16 |
| 33. | Check valve spring | 1 | 88. | Wheel | 2 |
| 34. | Check valve casing | 1 | 89. | Wheel | 2 |
| 35. | O-ring d10×1.8 | 1 | 90. | Chassis | 1 |
| 36. | Check valve screw | 1 | 91. | Pin axle | 4 |
| 37. | Spring base | 1 | 92. | Hex screw M6×12 | 4 |
| 38. | Spring | 1 | 93. | Bushing | 4 |
| 39. | Seal cover d18×D25×4.5 | 1 | 94. | Scissors lever | 1 |
| 40. | O-ring d18×2.65 | 1 | 95. | Retainer 16 | 5 |
| 41. | Pump plunger | 1 | 96. | Roller for chassis | 2 |
| 42. | Y-ring | 1 | 97. | Bushing | 4 |
| 43. | Pump body for plunger | 1 | 98. | Nut M10 | 2 |
| 44. | O-ring d28×3.1 | 1 | 99. | Spring washer 10 | 4 |
| 45. | Pump body | 1 | 100. | Washer 10 | 8 |
| 46. | O-ring d10.6×2.65 | 1 | 101. | Safety rod | 2 |
| 47. | Spring | 1 | 102. | Screw bolt M10×40 | 2 |
| 48. | Reflux rod | 1 | 103. | Spring pin 8×40 | 2 |
| 49. | O-ring d4×1.8 | 1 | 104. | Roller for table | 2 |
| 50. | Guide casing | 1 | 105. | table | 1 |
| 51. | Protect casing | 1 | 106. | Pin axle | 1 |
| 52. | Lever | 1 | A | Pump ass'y | 1～51 |
| 53. | Lever bushing | 1 | B | Swivel wheel ass'y | 89 |
| 54. | Washer 6 | 2 | C | Front wheel ass'y | 88 |
| 55. | Spring washer 6 | 5 | D | Seal kit ass'y 1,3,4,7,8,9,16,23, |  |
|  |  |  |  | 25,31,35,39,40,42,44,46,49 |  |
|  |  |  | E | Handle ass'y 54,57～64,68～72 |  |

BS50 & BS75

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover d30×D42×7 | 1 | 56. | Steel wire | 1 |
| 2. | Cylinder cover | 1 | 57. | Nut M8 | 24 |
| 3. | O-ring d63×2.65 | 2 | 58. | Washer 8 | 38 |
| 4. | O-ring d30×3.55 | 1 | 59. | Spring pin | 1 |
| 5. | Piston Rod | 1 | 60. | Spring pin | 1 |
| 6. | Spacing casing | 1 | 61. | Control link | 1 |
| 7. | Guide ring δ1.5×15 | 1 | 62. | Handle | 1 |
| 8. | O-ring D20×2.4 | 1 | 63. | Spacing casing | 2 |
| 9. | Seal ring d34×D40×4.5 | 1 | 64. | Spring washer 12 | 2 |
| 10. | Retainer for piston rod | 1 | 65. | Hex screw M12×40 | 2 |
| 11. | Spacing retainer 18 | 6 | 66. | Split pin 2×15 | 1 |
| 12. | Piston | 1 | 67. | Pin | 1 |
| 13. | Cylinder | 1 | 68. | U- fork | 1 |
| 14. | Washer for cylinder | 1 | 69. | Nut M6 | 1 |
| 15. | Reservior | 1 | 70. | Bolt | 1 |
| 16. | O-ring d10×2.65 | 1 | 71. | Pedal bent pipe | 1 |
| 17. | Filler screw | 1 | 72. | Hex soch screw M8×20 | 2 |
| 18. | Washer for reservior | 1 | 73. | Shake link | 1 |
| 19. | Steel ball 5 | 1 | 74. | Spring | 2 |
| 20. | Spring base | 1 | 75. | Retainer 10 | 2 |
| 21. | Regulating pressure spring | 1 | 76. | Pin axle | 2 |
| 22. | Regulating pressure screw | 1 | 77. | Link | 2 |
| 23. | O-ring d7.1×1.8 | 1 | 78. | Wheel | 2 |
| 24. | End cover | 1 | 79. | Nut M10 | 16 |
| 25. | O-ring d15×2.65 | 2 | 80. | Spring washer 10 | 16 |
| 26. | Regulating speed spring | 1 | 81. | Washer 10 | 36 |
| 27. | Regulating slide-valve | 1 | 82. | Hex soch screw M10×25 | 16 |
| 28. | Regulating speed spring casing | 1 | 83. | Wheel | 2 |
| 29. | Regulating speed slide-casing | 1 | 84. | axle | 1 |
| 30. | Steel ball 7 | 1 | 85. | Retainer 20 | 4 |
| 31. | O-ring d6.9×1.8 | 1 | 86. | Chassis | 1 |
| 32. | Conical valve | 1 | 87. | Table | 1 |
| 33. | Spring | 1 | 88. | Roller for table | 2 |
| 34. | Check valve casing | 1 | 89. | Bushing | 2 |
| 35. | O-ring d10×1.8 | 1 | 90. | Split pin 3.2×26 | 2 |
| 36. | Check valve screw | 1 | 91. | Nut M16 | 1 |
| 37. | Seal cover d18×D25×4.5 | 1 | 92. | Washing | 1 |
| 38. | O-ring d18×2.65 | 1 | 93. | Bushing | 2 |
| 39. | Pump plunger | 1 | 94. | Spring pin 8×40 | 2 |
| 40. | Y-ring | 1 | 95. | Screw bolt M10×40 | 2 |
| 41. | Pump body for plunger | 1 | 96. | Safety rod | 2 |
| 42. | O-ring D28×3.1 | 1 | 97. | Nut M10 | 2 |
| 43. | Pump body | 1 | 98. | External scissors lever | 1 |
| 44. | O-ring d10.6×2.65 | 1 | 99. | Bushing | 2 |
| 45. | Spring | 1 | 100. | Roller for chassis | 2 |
| 46. | Reflux rod | 1 | 101. | Internal scissors lever | 1 |
| 47. | O-ring d4×1.8 | 1 | 102. | Pin axle for chassis | 1 |
| 48. | Guide casing | 1 | 103. | Spring washer 8 | 2 |
| 49. | Protect casing | 1 | 104. | Hex screw M8×16 | 2 |
| 50. | Lever | 1 | 105. | Pin axle for scissons | 1 |
| 51. | Lever bushing | 1 | 106. | Pin axle for table | 1 |
| 52. | Washer 6 | 2 | 107. | Bushing | 2 |
| 53. | Spring washer 6 | 5 | 108. | Bolt M8×12 | 1 |
| 54. | Hex soch screw M6×16 | 1 | 109. | Oil cup | 2 |
| 55. | Tube for steel wire | 1 | 110. | Screw M6 | 1 |

| NO. | DESCRIPTION | Qty's | NO. | DESCRIPTION | Qty's |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover d35×D43.5×5 | 1 | 57. | Steel wire | 1 |
| 2. | Cylinder cover | 1 | 58. | Nut M8 | 24 |
| 3. | O-ring d75×3.55 | 1 | 59. | Washer 8 | 38 |
| 4. | O-ring d35.5×3.55 | 1 | 60. | Spring pin | 1 |
| 5. | Piston Rod | 5 | 61. | Spring pin | 1 |
| 6. | Spacing casing | 1 | 62. | Control link | 1 |
| 7. | Guiding δ2×15 | 1 | 63. | Handle | 1 |
| 8. | O-ring D20×2.4 | 1 | 64. | Spacing casing | 2 |
| 9. | Seal ring d39×D45×4.5 | 1 | 65. | Spring washer 12 | 2 |
| 10. | Retainer for piston rod | 1 | 66. | Hex screw M12×40 | 2 |
| 11. | Spacing retainer 18 | 6 | 67. | Split pin 2×15 | 1 |
| 12. | Piston | 1 | 68. | Pin | 1 |
| 13. | Cylinder | 1 | 69. | U- fork | 1 |
| 14. | Washer for cylinder | 1 | 70. | Nut M6 | 1 |
| 15. | Reservior | 1 | 71. | Bolt | 1 |
| 16. | O-ring d10×2.65 | 1 | 72. | Pedal bent pipe | 1 |
| 17. | Filler screw | 1 | 73. | Hex screw M8×20 | 2 |
| 18. | O-ring d75×2.65 | 1 | 74. | Shake link | 1 |
| 19. | Washer for reservior | 1 | 75. | Spring | 2 |
| 20. | Steel ball 5 | 1 | 76. | Pin axle | 2 |
| 21. | Spring base | 1 | 77. | Retainer 10 | 2 |
| 22. | Regulating pressure spring | 1 | 78. | Link | 2 |
| 23. | Regulating pressure screw | 1 | 79. | Table | 1 |
| 24. | O-ring d7.1×1.8 | 1 | 80. | Retainer 20 | 4 |
| 25. | End cover | 1 | 81. | Roller for table | 2 |
| 26. | O-ring d15×2.65 | 2 | 82. | Bushing | 2 |
| 27. | Regulating speed spring | 1 | 83. | Split pin 3.2×26 | 2 |
| 28. | Regulating slide-valve | 1 | 84. | Nut M16 | 2 |
| 29. | Regulating speed spring casing | 1 | 85. | Washing | 2 |
| 30. | Regulating speed slide-casing | 1 | 86. | Bushing | 2 |
| 31. | Steel ball 7 | 1 | 87. | Pin axle for scissors | 2 |
| 32. | O-ring d6.9×1.8 | 1 | 88. | Spring washer 8 | 3 |
| 33. | Conical valve | 1 | 89. | Hex screw M8×10 | 3 |
| 34. | Spring | 1 | 90. | Spring pin 8×40 | 2 |
| 35. | Check valve casing | 1 | 91. | Screw bolt M10×40 | 2 |
| 36. | O-ring d10×1.8 | 1 | 92. | Washer 10 | 34 |
| 37. | Check valve screw | 1 | 93. | Safety rod | 2 |
| 38. | Seal cover d18×D25×4.5 | 1 | 94. | Spring washer 10 | 34 |
| 39. | O-ring d18×2.65 | 1 | 95. | Nut M10 | 2 |
| 40. | Pump plunger | 1 | 96. | External scissors lever | 1 |
| 41. | Y-ring d10×D18×6 | 1 | 97. | Bushing | 2 |
| 42. | Pump body for plunger | 1 | 98. | Roller for chassis | 2 |
| 43. | O-ring D28×3.1 | 1 | 99. | Bushing | 2 |
| 44. | Pump body | 1 | 100. | Pin axle for chassis | 1 |
| 45. | O-ring d10.6×2.65 | 1 | 101. | Pin axle for table | 1 |
| 46. | Spring | 1 | 102. | Bushing | 2 |
| 47. | Reflux rod | 1 | 103. | Oil cup | 2 |
| 48. | O-ring d4×1.8 | 1 | 104. | Bolt M8×12 | 1 |
| 49. | Guide casing | 1 | 105. | Internal scissors lever | 1 |
| 50. | Protect casing | 1 | 106. | Chassis | 1 |
| 51. | Lever | 1 | 107. | axle | 1 |
| 52. | Lever bushing | 1 | 108. | Hex soch screw M10×25 | 16 |
| 53. | Washer 6 | 2 | 109. | Nut M10 | 16 |
| 54. | Spring washer 6 | 5 | 110. | Wheel | 2 |
| 55. | Hex soch screw M6×16 | 1 | 111. | Wheel | 2 |
| 56. | Tube for steel wire | 1 |  |  |  |

| NO. | DESCRIPTION | NO. | DESCRIPTION |
| --- | --- | --- | --- |
| 1. | Seal cover d30×D42×7 | 57. | Nut M8 |
| 2. | Cylinder cover | 58. | Washer 8 |
| 3. | O-ring d63×2.65 | 59. | Spring pin |
| 4. | O-ring d30×3.55 | 60. | Spring pin |
| 5. | Piston Rod | 61. | Control link |
| 6. | Spacing casing | 62. | Handle |
| 7. | Guiding δ1.5×15 | 63. | Spacing casing |
| 8. | O-ring D20×2.4 | 64. | Spring washer 12 |
| 9. | Seal ring d34×D40×4.5 | 65. | Hex screw M12×40 |
| 10. | Retainer for piston rod | 66. | Spcit pin |
| 11. | Spacing retainer 18 | 67. | Pin |
| 12. | Piston | 68. | U- fork |
| 13. | Cylinder | 69. | Nut M6 |
| 14. | Washer for cylinder | 70. | Bolt |
| 15. | Reservior | 71. | Pedal bent pipe |
| 16. | O-ring d10×2.65 | 72. | Hex headed bolt |
| 17. | Filler screw | 73. | Shake link |
| 18. | Washer for reservior | 74. | Spring |
| 19. | Steel ball 5 | 75. | Retainer ring for axle 10 |
| 20. | Spring base | 76. | Pin axle |
| 21. | Regulating pressure spring | 77. | Link |
| 22. | Regulating pressure screw | 78. | Wheel |
| 23. | O-ring d7.1×1.8 | 79. | Nut M10 |
| 24. | End cover | 80. | Spring washer 10 |
| 25. | O-ring d15×2.65 | 81. | Washer 10 |
| 26. | Regulating speed spring | 82. | Hex soch screw M10×25 |
| 27. | Regulating slide-valve | 83. | Wheel |
| 28. | Regulating speed spring casing | 84. | Pin axle |
| 29. | Regulating speed slide-casing | 85. | Retaining ring for axle 20 |
| 30. | Steel ball 7 | 86. | Chassis |
| 31. | O-ring d6.9×1.8 | 87. | Hex socket screw Bolt M8×16 |
| 32. | Conical valve | 88. | Pin axle |
| 33. | Spring | 89. | Bushing |
| 34. | Check valve casing | 90. | Washer |
| 35. | O-ring d10×1.8 | 91. | Slotting nut M16×1.5 |
| 36. | Check valve screw | 92. | Split pin |
| 37. | Seal cover d18×D25×4.5 | 93. | Pin axle |
| 38. | O-ring d18×2.65 | 94. | Pin axle |
| 39. | Pump plunger | 95. | Hex socket set screw M8×12 |
| 40. | Y-ring | 96. | Bushing |
| 41. | Pump body for plunger | 97. | Oil cup |
| 42. | O-ring D28×3.1 | 98. | External scissors lever for table |
| 43. | Pump body | 99. | Internal scissors lever for table |
| 44. | O-ring d10.6×2.65 | 100. | Bushing |
| 45. | Spring | 101. | Roller for table |
| 46. | Reflux rod | 102. | Table |
| 47. | O-ring d4×1.8 | 103. | Pin 8×40 |
| 48. | Guide casing | 104. | Hex headed screw bolt M10×40 |
| 49. | Protect casing | 105. | Safety rod |
| 50. | Lever | 106. | Nut M10 |
| 51. | Lever bushing | 107. | External scissors lever for chassis |
| 52. | Washer 6 | 108. | Internal scissors lever for chassis |
| 53. | Spring washer 6 | 109. | Bushing |
| 54. | Hex soch screw M6×16 | 110. | Roller for chassis |
| 55. | Tube for steel | 111. | Pin axle |
| 56. | Steel wire |  |  |

BS 50D

| Item No. | Description | Item No. | Description |
| --- | --- | --- | --- |
| 1 | Seal cover d35×D43.5×5 | 59 | Spring pin |
| 2 | Cylinder cover | 60 | Spring pin |
| 3 | O-ring d75×3.55 | 61 | Control link |
| 4 | O-ring d35.5×3.55 | 62 | Handle |
| 5 | Piston Rod | 63 | Spacing casing |
| 6 | Spacing casing | 64 | Spring washer 12 |
| 7 | Guiding δ2×15 | 65 | Hex screw M12×40 |
| 8 | O-ring D20×2.4 | 66 | Spcit pin |
| 9 | Seal ring d39×D40×4.5 | 67 | Pin |
| 10 | Retainer for piston rod | 68 | U- fork |
| 11 | Spacing retainer 18 | 69 | Nut M6 |
| 12 | Piston | 70 | Bolt |
| 13 | Cylinder | 71 | Pedal bent pipe |
| 14 | Washer for cylinder | 72 | Hex headed bolt |
| 15 | Reservior | 73 | Shake link |
| 16 | O-ring d10×2.65 | 74 | Spring |
| 17 | Filler screw | 75 | Retainer ring for axle 10 |
| 18 | Washer for reservior | 76 | Pin axle |
| 19 | Steel ball 5 | 77 | Link |
| 20 | Spring base | 78 | Wheel |
| 21 | Regulating pressure spring | 79 | Nut M10 |
| 22 | Regulating pressure screw | 80 | Spring washer 10 |
| 23 | O-ring d7.1×1.8 | 81 | Washer 10 |
| 24 | End cover | 82 | Hex soch screw M10×25 |
| 25 | O-ring d15×2.65 | 83 | Wheel |
| 26 | Regulating speed spring | 84 | Pin axle |
| 27 | Regulating slide-valve | 85 | Retaining ring for axle 20 |
| 28 | Regulating speed spring casing | 86 | Chassis |
| 29 | Regulating speed slide-casing | 87 | Hex socket screw Bolt M8×16 |
| 30 | Steel ball 7 | 88 | Pin axle |
| 31 | O-ring d6.9×1.8 | 89 | Bushing |
| 32 | Conical valve | 90 | Washer |
| 33 | Spring | 91 | Slotting nut M16×1.5 |
| 34 | Check valve casing | 92 | Split pin |
| 35 | O-ring d10×1.8 | 93 | Pin axle |
| 36 | Check valve screw | 94 | Pin axle |
| 37 | Seal cover d18×D25×4.5 | 95 | Hex socket set screw M8×12 |
| 38 | O-ring d18×2.65 | 96 | Bushing |
| 39 | Pump plunger | 97 | Oil cup |
| 40 | Y-ring | 98 | External scissors lever for table |
| 41 | Pump body for plunger | 99 | Internal scissors lever for table |
| 42 | O-ring D28×3.1 | 100 | Bushing |
| 43 | Pump body | 101 | Roller for table |
| 44 | O-ring d10.6×2.65 | 102 | Table |
| 45 | Spring | 103 | Pin 8×40 |
| 46 | Reflux rod | 104 | Hex headed screw bolt M10×40 |
| 47 | O-ring d4×1.8 | 105 | Safety rod |
| 48 | Guide casing | 106 | Nut M10 |
| 49 | Protect casing | 107 | External scissors lever for chassis |
| 50 | Lever | 108 | Internal scissors lever for chassis |
| 51 | Lever bushing | 109 | Bushing |
| 52 | Washer 6 | 110 | Roller for chassis |
| 53 | Spring washer 6 | 111 | Pin axle |
| 54 | Hex soch screw M6×16 | 112 | Bolt M6×8 |
| 55 | Tube for steel | A | Pump ass'y 1～49 |
| 56 | Steel wire | B | Swivel wheel ass'y 83 |
| 57 | Nut M8 | C | Front wheel ass'y 78 |
| 58 | Washer 8 | D | Seal kit ass'y 1,3,4,7,8,9,16,23, 25,31,35,37,38,,40,42,44,47 |
|  |  | E | Handle ass'y 52,55～62,66～70 |

BS80D

| NO. | DESCRIPTION | Qty's | NO. | DESCRIPTION | Qty's |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover d50×D58×5 | 1 | 59. | Nut M8 | 6 |
| 2. | Y-ring d50×D58×8.2 | 1 | 60. | Washer 8 | 5 |
| 3. | Cylinder cover | 1 | 61. | Spring | 1 |
| 4. | O-ring d56×2.65 | 1 | 62. | Tube for steel wire | 1 |
| 5. | Piston Rod | 1 | 63. | Steel wire | 1 |
| 6. | Bushing | 2 | 64. | Spring pin | 1 |
| 7. | Bushing | 1 | 65. | Spring pin | 1 |
| 8. | Pin axle | 1 | 66. | Control link | 1 |
| 9. | Snap Ring 50 | 1 | 67. | Handle | 1 |
| 10. | Cylinder | 1 | 68. | Spacing casing | 2 |
| 11. | Prevent burst valve | 1 | 69. | Spring washing 12 | 2 |
| 12. | Spring | 1 | 70. | Hex screw M12×40 | 2 |
| 13. | Seal ring 18 | 1 | 71. | Snap ring | 2 |
| 14. | Prevent burst joint | 1 | 72. | Spacing casing | 1 |
| 15. | Seal ring 14 | 4 | 73. | Pressure roller | 1 |
| 16. | High pressure Hose | 1 | 74. | Pressure roller pin | 1 |
| 17. | Joint | 2 | 75. | Pedal pivot pin | 1 |
| 18. | Split pin | 1 | 76. | Nut M6 | 2 |
| 19. | Adjust casing seat | 1 | 77. | Spring washer 6 | 2 |
| 20. | O-ring d18×2.4 | 1 | 78. | Hex socket screw bolt M6×50 | 2 |
| 21. | Adjust casing | 1 | 79. | Pedal rubber | 1 |
| 22. | Spring seat | 1 | 80. | Pedal holder | 1 |
| 23. | Spring | 1 | 81. | Wheel | 2 |
| 24. | Conical valve | 1 | 82. | Nut M10 | 16 |
| 25. | Check valve casing | 1 | 83. | Spring washer 10 | 16 |
| 26. | O-ring d6.9×1.8 | 1 | 84. | Washer 10 | 32 |
| 27. | Steel ball | 2 | 85. | Hex socket screw M10 | 16 |
| 28. | Plug | 1 | 86. | Wheel | 2 |
| 29. | O-ring d10×2.65 | 2 | 87. | Chassis | 1 |
| 30. | Regulating speed valve casing | 1 | 88. | Bolt M6×8 | 1 |
| 31. | O-ring d15×2.65 | 2 | 89. | Spring washer 8 | 1 |
| 32. | Regulating speed spring seat | 1 | 90. | Hex socket screw bolt M8×16 | 1 |
| 33. | Regulating speed spring | 1 | 91. | Table | 1 |
| 34. | Regulating speed slide-valve | 1 | 92. | Roller for table | 2 |
| 35. | O-ring d20×2.65 | 1 | 93. | Bushing | 2 |
| 36. | Y-ring d20×D28×5 | 1 | 94. | Retaining ring for axle 20 | 6 |
| 37. | Pump plunger | 1 | 95. | Internal scissors lever for table | 1 |
| 38. | Spring | 1 | 96. | External scissors lever for table | 1 |
| 39. | Spring | 1 | 97. | Pin axle | 3 |
| 40. | Pump body | 1 | 98. | Washer | 5 |
| 41. | Mesh | 1 | 99. | Split Pin | 5 |
| 42. | Washer D5 | 1 | 100. | Slotting nut M16×1.5 | 5 |
| 43. | Discharge spring | 2 | 101. | Internal scissors lever for chassis | 1 |
| 44. | O-ring d14×2.4 | 1 | 102. | Pin 8×40 | 2 |
| 45. | Plug | 1 | 103. | Hex headed screw bolt M8×40 | 2 |
| 46. | Discharge lever | 1 | 104. | Safety rod | 2 |
| 47. | O-ring d4×1.8 | 1 | 105. | Nut M10 | 2 |
| 48. | Discharge lever bushing | 1 | 106. | External scissors lever for chassis | 1 |
| 49. | O-ring d10.6×2.65 | 1 | 107. | Bushing | 10 |
| 50. | Hex socket screw bolt M6×16 | 1 | 108. | Bushing | 2 |
| 51. | Bushing | 1 | 109. | Roller for chassis | 2 |
| 52. | Discharge lever | 1 | 110. | Pin axle | 2 |
| 53. | Steel ball | 1 | 111. | Pin axle | 1 |
| 54. | Spring seat assembly | 1 | 112. | Pin axle | 1 |
| 55. | Regulating pressure spring | 1 | 113. | Hex socket set screw M8×12 | 2 |
| 56. | Regulating pressure nut | 1 | 114. | Oil cup | 3 |
| 57. | O-ring d8×1.8 | 1 | 115. | Bushing | 2 |
| 58 | Screw | 1 |  |  |  |