Instruction Manual

MB Series

Note: Owner/Operator must read and understand this instruction manual before using the hoist.

Congratulations for your excellent choice. Your new electric tool is manufactured in compliance with the best quality and reliability standards, ensuring you efficiency and safety for a long period of time.

# GENERAL SAFETY RULES

WARNING! Before using this electric tool, carefully read the general safety rules listed below.

- Your sockets must comply with safety rules.

In case your sockets are not suitable, they should be checked by a skilled electrician.

- Your socket plug must absolutely be grounded and your electric system must be supplied with a magneto cut-out safety.

- When the machine is running unwatched, be careful that children cannot reach it.

- Do not pull the electric cable to disconnect the plug.

- The machine shall be protected from frost and low temperatures.

- In case the machine cannot hoist a load, do not keep pressing the hoisting push-button: this means that the load exceeds the machine maximum capacity.

- The machine shall not be disassembled when running or connected to power.

- The machine shall not be operated when it is raining or storming.

- Do not stand under hoisted weights.

- Before starting the work, make sure that the steel cable is correctly winded around the reel and the pitch is equal to the cable diameter.

- OBSERVE THE MAXIMUM LOAD INDICATED ON THE HOIST, NOT THAT ON THE HOOK!

- Leave at least three turns of cable around the reel, so that the cable connection is not under stress.

- To avoid any danger, do not wind more than 15 mt of cable around the reel.

- In case the steel cable is worn out, it must be replaced only with a cable of same features manufactured by us. It can be found at all authorized service shops.

- Before starting the work, check that switches are in good operating conditions.

- In case the hoist stops during the lowering of a load, it is normal that the load goes down a few centimeters more because of inertia.

-ATTENTION!! THE HOIST ELECTRIC MOTOR IS NOT SUPPLIED WITH ANY OVERLOAD CUT-OUT (TO AVOID AN UNEXPECTED AND UNWANTED RE-START) THEREFORE, IF YOU ARE UNABLE TO HOIST A LOAD DO NOT INSIST AND LET THE MOTOR COOL DOWN.

The hoist 《STANDARD VERSION》 is provided with a specially designed bracket system which allows to hold pipes box.

Check that socket features (volt-hertz) correspond to those indicated on the machine plate; then, you can insert the plug.

In case a cable extension is needed, it is absolutely important to respect the table's data.

| Extension Length | El cable section |
| --- | --- |
| Up to 20m | 1.5mm |
| 20 to 50 | 2.5mm |

## MAINTENANCE

- Periodically CHECK that the steel cable is in good conditions.

- CHECK that the screws securing the brackets and reduction gear are well tightened.

- CHECK THE CONDITIONS AND TIGHTENING OF THE NUTS securing the steel cable clamps.

- Periodically CHECK that motor stop switch and push button switch are in good operating conditions.

These descriptions and illustrations are not binding the firm reserves the right to modify them without any notice.

| No. | Description | No. | Description |
| --- | --- | --- | --- |
| 1 | Hexagon bolt | 35 | Safety switch |
| 2 | Spring washer | 36 | Breaker contactor |
| 3 | Flat washer | 37 | Locating pin |
| 4 | Fixing ring | 38 | Spring tab |
| 5 | Support structure | 39 | Cable |
| 6 | Rope roll shaft | 40 | Socket |
| 7 | Flat key | 41 | Holding fixture |
| 8 | Flat key | 42 | Capacitor |
| 9 | Elastic collar | 43 | Arm switch lower cover |
| 10 | Bearing | 44 | Arm switch upper cover |
| 11 | Hexagon fillister head screw | 45 | Rise and fall switch |
| 12 | Gear case | 46 | Three-prong plug |
| 13 | Spring washer | 47 | Locknut |
| 14 | Flat washer | 48 | Hook washer |
| 15 | Gearwheel | 49 | Hexagon bolt |
| 16 | Cushion board | 50 | Hexagon bolt |
| 17 | Front cover | 51 | Wheel axle |
| 18 | Bearing | 52 | Splint |
| 19 | Stator | 53 | Pulley |
| 20 | Stator shell | 54 | Hook fixed nut |
| 21 | Rotor | 55 | Gearwheel |
| 22 | Tripping spring | 56 | Flat key |
| 23 | Brake component | 57 | Gear shaft |
| 24 | Aft closure | 58 | Bearing |
| 25 | Fan blade | 59 | Hexagon fillister head screw |
| 26 | Fan cover | 60 | Limiter |
| 27 | Spring washer | 61 | Hook |
| 28 | Flat washer | 62 | Rope thimble |
| 29 | Hexagon bolt | 63 | Wire rope |
| 30 | Junction box | 64 | Block |
| 31 | Terminal | 65 | Aluminum |
| 32 | Cover | 66 | Rope roll |
| 33 | Holding fixture | 67 | Wedge |
| 34 | Holding fixture | 68 | Bushing |