# INSTRUCTION MANUAL

## HAND STACKER PA1015

## Capacity 1000kg

Note: The Owner/Operator must read carefully and understand all the information presented here before operation.

IMPORTANT

Please read, understand and follow these safety rules and operating instructions before operating this machine. Only trained and authorized personnel should be permitted to operate this machine. Please replace Part No. 138 with hole prior to use. (See P9)

l. Safety Rules

Failure to obey tile instructions and safety rules in this manual may result in death or serious injury.

1.1 Do Not Operate Unless:

1 ) You learn and practice the principles of safe machine operation contained in this operating manual.

――Avoid hazardous situations.

――Always perform a pre-operation inspection.

――Always perform the function tests prior to use.

――Inspect the workplace.

――Only use the machine as a material lift.

2) You read, understand and obey:

――Manufacturer's instructions and safety rules

――Employee's safety rules and worksite regulations

――Applicable governmental regulations

1.2 To Avoid Hazardous Situations:

1) Fall Hazards

Do not use as a personnel lifting platform or step.

Do not load unstable or loosely stacked loads.

2) Tip-over Hazards

Do not overload the machine. Check load diagram on the machine for different centered capacity machine.

Do not raise the load unless the machine is on a firm, level surface.

Do not move the machine with a raised load, except for minor positioning.

Do not operate the machine in strong or gusty winds.

Prior to use, check the work area for drop-offs, holes, bumps, debris, unstable surfaces or other possible hazardous conditions.

Do not subject the machine to horizontal force by raising or lowering a fixed or overhanging load.

3) Collision hazards

Do not lift if the load is not properly centered on the forks. Check load diagram on the machine for correct load center position.

Check the work area for overhead obstruction or other possible hazards.

Do not stand under or allow personnel under the machine when the load is raised.

Do not lower tile load unless the area below is clear of personnel and obstructions.

4) Bodily Injury Hazard

Always keep hands and fingers away from pulleys, the carriage and other potential pinch points.

5) Improper Use Hazard

Never leave a machine unattended with a load. Unauthorized     personnel may attempt to operate the machine without proper instruction creating an unsafe situation.

6) Damaged Machine Hazards

Do not use a damaged or malfunctioning machine.

Do not use a machine with a worn, damaged or more than 3% elongation chain.

Be sure that all decals arc in place and legible.

Maintain proper lubrication of chain and other movable parts.

7) Lifting Hazard

Use proper lifting techniques to load the machine.

2. Pre-operation Inspection

The operator should perform a visual inspection prior to each work shift to discover if anything is wrong with a machine.

2.1 Be sure that the instruction manual is complete, legible and available for reference.

2.2 Be sure that all decals are legible and in place.

2.3 Checking the following components or areas for damage and improperly installed, loose or missing parts:

~      Pump Unit and Related Components

~      Base Compo~ loll! S

~      Legs

~      Rollers

~      Frame

~      Chain and Pulleys

~      Casters

~      Forks

~      Brake System

~      Handle

~      Nuts, Bolts and Other Fasteners

2.4 Check entire machine for:

~      Dents or damage

~      Corrosion or oxidation

~      Cracks in welds or structural components

3. Function Tests

The operator must follow the step-by-step instructions to test all machine functions.

3.1 Test the Brake Operation

1) Press down on the foot pedal to lock the brake.

2) Push the machine. The machine should not move.

3) Pull up on the foot pedal to release the brake.

4) Push the machine. It should now move freely.

3.2 Test the Control Lever Functions

1) Set the control lever in the ASCENT position.

The carriage should rise to the top of the mast while pumping the handle.

The carriage should move smoothly, free of hesitation and binding.

2) Set the control lever in the NEUTRAL position.

The carriage should not rise or lower while pumping the handle.

3) Set the control lever in the LOWER position.

The carriage should lower into the mast. The carriage should move smoothly, free of hesitation and binding.

Note: A damaged or malfunctioning machine must never be used. If damage       or malfunctions are discovered during pre-operation inspection or function tests, the machine must be tagged and removed from service. Repairs to the machine may only be made by a qualified service technician and according to the manufacturer’s instructions. After repairs are completed, the operator must perform a pre-operation inspection and function test again before putting the machine into service.

4.Workplace inspection

To operate the machine safely, the operator should inspect the workplace     prior to moving the machine to the workplace.

Be aware of and avoid the following hazardous situations:

1) Drop-offs or holes

2) Bumps and floor obstructions

3) Debris

4) Overhead obstructions and high voltage conductors

5) Hazardous locations

6) Inadequate surface support to withstand all load forces imposed by the machine

7) Wind and weather conditions

8) All other possible unsafe conditions

5. Operating Instructions

Using the machine for any purpose other than lifting material is unsafe.

5.1 Raising and Lowering Load

1) Please load centrally across the forks. Check the load diagram oil tile machine for correct load center position.

2) Raise the load by pumping the handle ill the ASCENF position.

3) Lower the load by setting the control lever in the LOWER position.

5.2-Moving Machine with a Load

It is best to move the machine without load. Moving a raised load should    be restricted to positioning for loading and unloading. If it is necessary to move the machine with a raised load, understand and obey the following safety rules:

1) Area is level and clear of obstructions.

2) Load is correctly centered on the forks.

3) Avoid sudden starts and stops.

4) Travel with load in the lowest possible position.

5) Do not tilt the machine back with a raised load by pulling the C-shape handle on the mast.

6) Keep personnel away from machine and load.

5.3 Moving Machine on Small Slopes

The machine shall not be used on gradients. If it is necessary to negotiate     small slopes for the purposes of moving the truck between buildings    etc., understand and obey the following safety rules:

1. The gradient shall be no more than 2%.

2. The machine shall be unloaded.

3. The forks shall be facing downgrade.

5.4 Actual Operating Capacity

The actual operating capacity of the machine is the responsibility of the user. It may depend on the operator, floor and machine conditions and     frequency of the load handling cycle.

If the load exceeds the actual operating capacity, the operator must be assisted by one or more persons.

6. Maintenance

6.1 Periodic Maintenance

Periodic maintenance will prolong the lifetime of the machine.

See the table below for period of maintenance.

| Item | Check | Period |
| --- | --- | --- |
|  |  | 1 month | 6 months | 12 months |
| Frame | Check the loading parts |  | · |  |
| Wheels | Check wearing bearing and bearing housing | · |  |  |
| Turning | Check whether it turns properly | · |  |  |
| Hydraulic unit | Oil level Change oil Check safety |  | · | · · |
| Lifting chain | Check the extension rate and wear | · |  |  |
| Brake | Check whether it functions properly | · |  |  |
| Moveable parts | Check lubrication and tear | · |  |  |

6.2 Oil

1) Add oil

If the forks do not lift to maximum height, you should add oil. Restore the fluid level in the reservoir to 2mm below the oiling hole, this must be with the forks in the lowered position.

2) Change oil

Drain the oil in pump unit off. Then add oil as item 1 ).

3) Use the hydraulic type oil according to the temperature scale below.

| Temperature | Oil |
| --- | --- |
| -20℃－40℃ | L-HM46 Hydraulic oil (equivalent to ISO VG46) |

6.3 How To Expel Air Form The Pump Unit

Air may enter the unit when the seals are replaced. Lift the control lever to the LOWER position, and then move the handle up and down for dozens of times.

7. Troubles shooting

| No. | Trouble | Cause | Action |
| --- | --- | --- | --- |
| 1 | The forks do not lift to maximum height. | Not enough hydraulic oil. | Add more oil. |
| 2 | The forks do not lift up. | Not enough hydraulic oil. The oil has impurities. Discharge valve is out of adjustment. Air in the hydraulic oil. | Add more oil. Change the oil. Adjust the setting screw(140M). Expel the air(see item 6.3). |
| 3 | The forks do not descend. | The rod(1301) is deformed resulting from seriously unbalanced load. A part has been broken or been deformed resulting from unbalanced load. The setting screw(140M) is not in the correct position. | Replace the rod (1301). Repair or replace component. Adjust the setting screw (140M). |
| 4 | Leaks | Seals worn out or damaged. Some parts may be cracked or worn out. | Replace seals with new ones. Check and replace with new ones. |
| 5 | The forks descend without being lowered. | Impurities in the oil cause the discharge valve(B) to fail to close. Air in the oil. Seals worn or damaged. Discharge valve(B) is out of adjustment. | Replace with filtered oil. Expel the air(see item 6.3). Replace with new ones. Adjust the setting screw(140M). |

Note: Do not attempt to repair the hand hydraulic stacker unless you are trained and authorized to do so.

8.Specifications

Model											PA1015

Capacity											1000kg

Maximum fork height							1500mm

Minimum fork height							88mm

Fork width											160mm

Fork length										1150mm

Overall fork width								fixed: 540mm

adjustable: 346~710mm

Load roller											φ80 x 70mm

Steering wheel									φ150 x 50mm

Overall length									1604mm

Overall width									794mm

Overall height									1964mm

Net weight											220kg

Parts List of Handle

| Parts No. | Description | Q’ty | Parts No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| H1101 | Handle | 1 | H102 | Spring pin |  |
| H1102 | Rod and chain | 1 | H103 | Spring leaf | 1 |
| H1103 | Nut | 1 | H104 | Spring pin | 2 |
| H1104 | Nut | 1 | H105 | Spring pin | 1 |
| H1105 | Spring pin | 1 | H106 | Control lever | 1 |
| H1106 | Pin | 1 | H108 | Rubber cushion | 1 |
| H1107 | Axle | 1 | H111 | Nylon roller | 1 |
| H1108 | Steel roller | 1 | H112 | Spring pin |  |
| H1109 | Retaining ring | 2 |  |  |  |

Parts List of Pump Unit (Standard)

| Parts No. | Description | Q’ty | Parts No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| 1101 | Dust proof ring | 1 | 1155A | Seal ring | 1 |
| 1102 | Cylinder | 1 | 110 | Screw | 1 |
| 1103 | O-ring | 1 | 111 | Red copper washer | 1 |
| 1104 | O-ring | 1 | 112 | Spring | 1 |
| 1105 | Seal ring | 1 | 113 | Pressure rod | 1 |
| 1106 | Spacing washer | 1 | 114 | Steel ball | 1 |
| 1107 | O-ring | 1 | 115Q | Pressure valve body | 1 |
| 1108 | Rod | 1 | 116 | Split ring | 1 |
| 1109 | Guide casing | 1 | 166 | Retainer | 3 |
| 1110 | Washer | 1 | 117 | O-ring | 2 |
| 1111 | Retaining ring | 1 | 118 | Red copper washer | 2 |
| 1112(138) | Screw | Each 1 | 119 | Steel needle | 1 |
| 1113 | Welded bond | 1 | 121 | Spring pin | 1 |
| 1114 | Pressure cap | 1 | 129 | Steel ball | 1 |
| 1115 | Spring pin | 1 | 130Q | Discharge valve body | 1 |
| 1117 | Spring | 1 | 131 | Spring | 1 |
| 1134 | O-ring | 1 | 132 | O-ring | 1 |
| 1135 | Red copper washer | 1 | 167 | Retainer | 1 |
| 1136 | Bushing | 2 | 133 | Discharge valve shaft | 1 |
| 1137 | Bolt | 4 | 134 | Valve taper core | 1 |
| 1139 | Spring washer | 4 | 135 | Spring | 1 |
| 1140 | Plain washer | 4 | 136 | Pressure regulating screw | 1 |
| 1150A | Spring cover | 1 | 137 | O-ring | 2 |
| 1151A | Pump rod | 1 | 138 | Screw | 1 |
| 1152A | Dust proof ring | 1 | 139M | Crank link | 1 |
| 1153A | O-ring | 1 | 140M | Setting screw | 1 |
| 1154A | Pump cylinder | 1 | 141 | Nut | 1 |

| Parts No. | Description | Q’ty | Parts No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| 1101 | Dust proof ring | 1 | 1134 | O-ring | 1 |
| 1102 | Cylinder | 1 | 1135 | Red copper washer | 1 |
| 1103 | O-ring | 1 | 1136 | Bushing | 2 |
| 1104 | O-ring | 1 | 1137 | Bolt | 4 |
| 1105 | Seal ring | 1 | 1139 | Spring washer | 4 |
| 1106 | Spacing washer | 1 | 1140 | Plain washer | 4 |
| 1107 | O-ring | 1 | 110 | Screw | 1 |
| 1108 | Rod | 1 | 111 | Red copper washer | 1 |
| 1109 | Guide casing | 1 | 112 | Spring | 1 |
| 1110 | Washer | 1 | 113 | Pressure rod | 1 |
| 1111 | Retaining ring | 1 | 114 | Steel ball | 1 |
| 1112(138) | Screw | Each 1 | 115Q | Pressure valve body | 1 |
| 1113 | Welded bond | 1 | 116 | Split ring | 1 |
| 1114 | Pressure cap | 1 | 166 | Retainer | 3 |
| 1115 | Spring pin | 1 | 117 | O-ring | 2 |
| 1116 | Spring cover | 1 | 118 | Red copper washer | 2 |
| 1117 | Spring | 1 | 119 | Steel needle | 1 |
| 1118 | Screw | 1 | 121 | Spring pin | 1 |
| 1119 | O-ring | 1 | 129 | Steel ball | 1 |
| 1120 | Pressure regulating screw | 1 | 130Q | Discharge valve body | 1 |
| 1121 | Dust proof ring | 1 | 131 | Spring | 1 |
| 1122 | Pump cylinder | 1 | 132 | O-ring | 1 |
| 1123 | O-ring | 1 | 167 | Retainer | 1 |
| 1124 | Seal ring | 1 | 133 | Discharge valve shaft | 1 |
| 1125 | Pump rod | 1 | 134 | Valve taper core | 1 |
| 1126 | Seal ring | 1 | 135 | Spring | 1 |
| 1127 | Spring | 1 | 136 | Pressure regulating screw | 1 |
| 1128 | Steel ball | 2 | 137 | O-ring | 2 |
| 1129 | Spring | 2 | 138 | Screw | 1 |
| 1130 | Pressure rod | 1 | 139M | Crank link | 1 |
| 1131 | Steel ball | 1 | 140M | Setting screw | 1 |
| 1132 | O-ring | 1 | 141 | Nut | 1 |
| 1133 | Valve seat | 1 |  |  |  |

Parts List of Pump Unit (Quick Lift)

Parts List of Frame (Fixed)

| Parts No. | Description | Q’ty | Parts No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| F1101 | Safety net | 1 | F1128 | Carriage | 1 |
| F1102 | Screw | 6 | F1129 | Retaining ring | 6 |
| F1103 | Washer | 6 | F1130 | Bearing | 6 |
| F1104 | Frame | 1 | F1131 | Roller | 4 |
| F1105 | Spacing plate | 1 | F1132 | Axle | 4 |
| F1106 | Rubber cushion | 1 | F1133 | Bolt | 4 |
| F1107 | Hexagon nut | 4 | F1134 | Washer | 4 |
| F1108 | Self-locking nut | 2 | F1135 | Bolt | 2 |
| F1109 | Bolt | 4 | F1136 | Bolt | 2 |
| F1110 | Spring washer | 2 | F1137 | Chain | 2 |
| F1111 | Washer | 2 | F1138 | Retaining ring | 2 |
| F1112 | Casing | 2 | F1139 | Chain pulley | 2 |
| F1113 | Bearing | 2 | F1140 | Chain pulley bracket | 1 |
| F1113A | Bearing | 2 | F1141 | Pivoted axle (single) | 2 |
| F1114 | Casing | 2 | F1142 | Load roller (single) | 2 |
| F1115 | Steering wheel bracket | 2 | F1146 | Split pin | 4 |
| F1116 | Self-locking nut | 2 | F113 | Adjustable bracket | 2 |
| F1117 | Nut | 2 | F114 | Load roller axle (tandem) | 4 |
| F1118 | Foot pedal | 2 | F116 | Load roller (tandem) | 4 |
| F1119 | Steering wheel axle | 2 | 1004 | Bolt | 2 |
| F1120 | Pin | 2 | 1005 | Retaining ring | 4 |
| F1121 | Spring leaf | 2 | 1006 | Roller bracket | 2 |
| F1122 | Casing | 4 | 1007 | Roller | 4 |
| F1123 | Bearing | 12 | 1008 | Nut | 2 |
| F1124 | Steering wheel | 2 | 1009 | Roller axle | 4 |
| F1125 | Spring pin | 6 | 1031 | Bolt | 4 |
| F1126 | Pivoted axle | 2 | 1032 | Nut | 4 |
| F1127 | Type U block | 1 |  |  |  |

Parts List of Frame (Adjustable)

| Parts No. | Description | Q’ty | Parts No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| F1101 | Safety net | 1 | F1129 | Retaining ring | 6 |
| F1102 | Screw | 6 | F1130 | Bearing | 6 |
| F1103 | Washer | 6 | F1131 | Roller | 4 |
| F1104 | Frame | 1 | F1132 | Axle | 4 |
| F1105 | Spacing plate | 1 | F1133 | Bolt | 4 |
| F1106 | Rubber cushion | 1 | F1134 | Washer | 4 |
| F1107 | Hexagon nut | 4 | F1135 | Bolt | 2 |
| F1108 | Self-locking nut | 2 | F1136 | Bolt | 2 |
| F1109 | Bolt | 4 | F1137 | Chain | 2 |
| F1110 | Spring washer | 2 | F1138 | Retaining ring | 2 |
| F1111 | Washer | 2 | F1139 | Chain pulley | 2 |
| F1112 | Casing | 2 | F1140 | Chain pulley bracket | 1 |
| F1113 | Bearing | 2 | F1141 | Pivoted axle (single) | 2 |
| F1113A | Bearing | 2 | F1142 | Load roller (single) | 2 |
| F1114 | Casing | 2 | F1143 | Spring pin | 2 |
| F1115 | Steering wheel bracket | 2 | F1144 | Shaft | 1 |
| F1116 | Self-locking nut | 2 | F1145 | Adjustable fork | 2 |
| F1117 | Nut | 2 | F1146 | Split pin | 4 |
| F1118 | Foot pedal | 2 | F113 | Adjustable bracket | 2 |
| F1119 | Steering wheel axle | 2 | F114 | Load roller axle (tandem) | 4 |
| F1120 | Pin | 2 | F116 | Load roller (tandem) | 4 |
| F1121 | Spring leaf | 2 | 1004 | Bolt | 2 |
| F1122 | Casing | 4 | 1005 | Retaining ring | 4 |
| F1123 | Bearing | 12 | 1006 | Roller bracket | 2 |
| F1124 | Steering wheel | 2 | 1007 | Roller | 4 |
| F1125 | Spring pin | 6 | 1008 | Nut | 2 |
| F1126 | Pivoted axle | 2 | 1009 | Roller axle | 4 |
| F1127 | Type U block | 1 | 1031 | Bolt | 4 |
| F1128A | Carriage | 1 | 1032 | Nut | 4 |