# Instruction Manual

Gator Grip Forklift Drum Grab

Note: The Owner/Operator must read carefully and understand

all the information presented here before operation.

THANK YOU FOR USING THIS GATOR GRIP FORKLIFT DRUM GRAB. FOR YOUR SAFETY AND CORRECT OPERATION, PLEASE CAREFULLY READ THIS INSTRUCTION BEFORE USING IT.

NOTE: All of the information reported herein is based on data available at the moment of printing. The factory reserves the right to modify its own products at any moment without notice and incurring in any sanction. So it is suggested to always verify possible updates.

DG720 is designed for grabbing and transport the drums as an attachment to the forklift. It can grab two 55 gallons drums, the max capacity is 720kg.

For your safety and correct operation, please carefully read this instruction before using it.

If you have any questions after reading this manual, please contact your supplier in time.

- PACKING

DG720A drum grab is packed with soft material. Please check carefully whether there is something damaged because of transporting or other problems when opening the packing. If does, please fill in the complaint list and send it to your provider.

- REQUIREMENT OF SAFETY OPERATION

Warning: DG720A drum grab is designed for special usage. Please pay attention to the following items to ensure your proper operation.

  - The rated capacity of this drum grab is 720kg.

  - Never overload the forklift beyond it rated capacity.

  - It is designed for catching the drum. You must tighten the drum cover before grabbing it.

  - Contact the fork manufacturer to choose suitable fork feet before use.

  - Never lift a person or other goods.

  - Do not lift the drum for a long time.

  - Do not ruin or tear the warning label.

  - Please check carefully before use. Repair it in time if it is damaged somewhere.

  - Do not modify this product without the permission of the manufacture.

- OPERATING INSTRUCTIONS

  - Installation: Put the grab on the flat ground, adjust the distance between two fork feet to fit the slot of the grab.

  - Tighten the T-bolt manually or with a tool, or button the eyebolt on the forklift with chains. Check the T-bolt regularly to make sure it is not loose.

  - Forklift lift the grab near the drum and grab the top brim of the drum, then the grab will hold the drum when forklift rise gradually, then you can move the drum.

  - The grab will separate automatically when the drum had been laid down.

  - When lifting two drums, try to get them close and ensure their weights are similar to keep their balance.

  - The grab is designed as a spring structure. It won’t separate automatically even if loosing the gravity when bumping.

- MAINTENANCE

Please lubricate active parts regularly.

- RESPONSIBILITY

Contact the supplier in 9 days if there is something wrong with the product.

- LIMITED RESPONSIBILITY

The manufacturers disclaim all responsibility for the damage caused by misuse, wrong operation or not following the instructions.

- ORDER COMPONENT

Please contact your supplier when you want to order some component.

- PARAMETER

| Type | Capacity | Drum type | Weight |
| --- | --- | --- | --- |
| DG720A | 720 kg | 210 | 96 kg |