# Instruction  Manual

## Pallet Truck with Scale

## Type A

Note: Owner/Operator must read and understand this instruction manual before using the pallet truck with scale.

Thank you for using this hand pallet truck with scale. For your safety and correct operation, please carefully read this instruction before using it.

NOTE: (1) All of the information reported herein is based on data available at the moment of printing. The factory reserves the right to modify its own products at any moment without notice and incurring in any sanction. So it is suggested to always verify possible updates.

(2) Prior to use this hand pallet truck with scale, the battery of scale must be charged enough.

- GENERAL SPECIFICATIONS

| Model | Capacity | Weighing Accuracy | Fork size | Net weight |
| --- | --- | --- | --- | --- |
|  |  |  | Length | Width over forks | Fork Width |  |
| HPW20S | 2000kg | ±1‰ | 1150mm | 555mm | 180mm | 136kg |
| HPW20L | 2000kg | ±1‰ | 1150mm | 690mm | 180mm | 143kg |

Materials and specification are subject to change without notice.

2. TO ATTACH HANDLE TO PUMP UNIT

2.1 Loosen the setting screw (140H) on the crank link (139H).

2.2 Remove three screws (H109) and three spring washers (H110) from the base (103).

2.3 Place the handle (H101) on the base (103), please note: Feed the rod and chain (H107) through the centre of the base (103) and axle (109).

2.4 Insert three screws (H109) with spring washers (H110) into the base (103). Then tighten them securely.

2.5 Raise the crank link (139H) and put the pin on rod and chain (H107) into the groove of crank link (139H).

3. TO ADJUST RELEASE DEVICE

On the handle of the pallet truck, you will find the control lever (H106) which can be set in three positions (See Fig. 1):

LOWER=to lower the forks; NEUTRAL=to move the load; ASCENT=to raise the forks. After assembling the handle, you can adjust the three positions.

3.1 First tighten the setting screw (140H) on the crank link (139H) until the LOWER position function works.

3.2 If the forks elevate while pumping in the NEUTRAL position, turn the setting screw (140H) clockwise until pumping the handle does not raise the forks and the NEUTRAL position functions correctly.

3.3 If the forks descend while pumping in the NEUTRAL position, turn the setting screw (140H) counter-clockwise until the forks do not lower.

3.4 If the forks do not descend when the control lever (H106) is in the LOWER position, turn the setting screw (140H) clockwise until raising the control lever (H106) lowers the forks. Then check the NEUTRAL position as per item 3.2 and 3.3.

3.5 If the forks do not lift while pumping in the ASCENT position, turn the setting screw (140H) counter-clockwise until the forks elevate while pumping in the ASCENT position. Then check the NEUTRAL and LOWER position as per item 3.2, 3.3 and 3.4.

- MAINTENANCE

4.1 OIL

Please check the oil level every six months. The volume of oil is about 0.3lt.

Use the hydraulic type oil according to temperature scale below.

| Temperature | Oil |
| --- | --- |
| -5℃~+45℃ | L-HM68 Hydraulic oil (equivalent to ISO VG68) |
| -15℃~-5℃ | L-HM46 Hydraulic oil (equivalent to ISO VG46) |

4.2 HOW TO EXPEL AIR FROM THE PUMP UNIT

The air may come into the hydraulic because of transportation or pump in upset position. It can cause that forks do not elevate while pumping in the ASCENT position. The air can be banished in the following way: Let the control lever (H106) to the LOWER position, then move the handle (H1501) up and down for several times.

4.3 DAILY CHECK AND MAINTENANCE

Daily check of the pallet truck can limit wear as much as possible. Give special attention to the wheels (127, F116 or F117), the axles (F114, F118, F121, F122), the handle (H101), the forks (F110) and lift and lower control. The forks should be unloaded and lowered in the lowest position when the job is over.

4.4 LUBRICATION

Use motor oil or grease to lubricate all moveable parts.

5. GUIDE TO SAFETY OPERATION

For safe operation of the truck, please read all warning signs and instructions here and on the truck before using this truck.

5.1 Do not operate the pallet truck unless you are familiar with it and have been trained or authorised to do so.

5.2 Do not operate the truck unless you have checked its condition. Give special attention to the wheels, the handle assembly, the forks, lift and the lower control.

5.3 Do not use the truck on sloping ground.

5.4 Never place any part of your body in the lifting mechanism or under the forks or load. Do not carry passengers.

5.5 The operator had better take on wear gloves and security shoes for labor protecting.

5.6 Do not handle unstable or loosely stacked loads.

5.7 Do not overload the truck.

5.8 Do not subject to unbalanced load, either side to side or along the length of the frame (refer to Fig. 2/B).

5.9 The capacity of the truck assumes an evenly distributed load with the centre of the load being at the halfway point of the length of the forks.

5.10 Make sure that length of the forks matches the length of the pallet.

5.11 Lower the forks to lowest height when the truck is not being used.

5.12 At other specific conditions or places, the operator should be carefully to operate the pallet truck.

2

6. TROUBLES SHOOTING

| NO | TROUBLE | CAUSE | SHOOTING |
| --- | --- | --- | --- |
| 1 | The forks can’t rise to max. height. | -The hydraulic oil is not enough . | - Pour in enough filtered oil. |
| 2 | The forks do not lift up. | -Without hydraulic oil. -The oil has impurities. -Discharge valve is out of adjustment. -Air in the hydraulic oil. | -Pour in more filtered oil. -Change the oil. -Adjust the setting screw (140H) (See item 3.5). -Banish the air (See item 4.2). |
| 3 | The forks can’t be descend. | -The rod (102) and the cylinder (159H) becomes deformed result from serious unbalanced load. -Component deformation result from unbalanced load. -The forks were kept at high position for long time with rod (102) bared and got rusty. -The setting screw (140H) is not in the correct position. | -Replace the rod (102) or cylinder (159H). -Repair or replace component to make it run smoothy. -Remove the rust on the rod (102). Keeping the forks at lowest position if not being used. -Adjust the setting screw (140H) (See item 3.4) |
| 4 | Leaks | -Seals worn out or damaged. -Some parts may be cracked or worn out. | -Replace seals with new ones. -Check and replace with new ones. |
| 5 | The forks descend without being lowered. | -Impurities in the oil cause the discharge valve (B) to fail to close. -Air in the oil. -Seals worn or damaged. -Discharge valve (B) is out of adjustment. | -Replace with filtered oil. -Expel the air (See item 4.2). -Replace with new ones. -Adjust the setting screw (140H) (See item 3.3). |

*NOTE: DO NOT ATTEMPT TO REPAIR THE PALLET TRUCK UNLESS YOU

ARE TRAINED AND AUTHORIZED TO DO SO.

- WEIGHING OPERATION

7.1 Preparation:  
   Put the control lever in the LOWER position and lower the truck to lowest position.

  - Press the “Print” key until the backlight on. After the indicator being checked by itself, it  display “0kg”.

  - Weighing method for gross weight:

Put the forks under pallet and judge by eyes it will be balanced load. Put the control lever in the ASCENT position, pump the handle to make the fork rise, until you can make sure the pallet leave ground. The stable reading of the indictor is the gross weight of the goods (total weight of the pallet and the goods).

  - Net weight weighing method

To weigh the goods packed in the same type standard pallet, please operate as following:

7.4.1 Weigh single standard pallet, for example: weight of pallet: 40kg.

7.4.2 Press the key of “TARE”, then the indicator display “0kg”.

7.4.3 Remove the pallet from the fork, then the indicator display “-40kg”.

7.4.4 Weigh the palletized goods according the method of 7.3, the stable reading of the indicator is the net weight of the goods.

  - The Switch of kilogram and pound.

When the reading of indicator is in unit of kilogram, press the key of “FUNCTION”, the unit of reading switch to pound. Press the key of “FUNCTION” again, the unit of reading switch to kilogram again.

  - Turn off the Indicator

When the indicator woks normally, press the key of “PRINT” until the indicator display “OFF”. Loosen the key will turn off the indicator.

Remark:

The service manual of indicator is appendix of this manual. If you need detailed information about technical features, installation, operation, programming, and configuration, maintenance of the indicator, calibration of scale.

8. BATTERY POWER DATA AND REPLACEMENT

The HAWK indicator on scale pallet truck adopts six “D” size batteries as DC power. You are recommended to use alkaline battery. Also you can use rechargeable battery. As the HAWK can’t be used as a charger.

Change the batteries when the illuminated cursor points to the “Low battery icon” displayed as  +   -  on the keyboard of indicator.

How to change batteries:

8.1 Loosen the knurled screw (F309) on the two sides of indicator case (F308), turn over the baffle of indicator case.

8.2 Open the battery cover plate on the rear of indicator (F310), insert six “D” size batteries into the battery holder according to the direction marked in the holder. Then install the battery cover plate.

8.3 Screw the knurled screw to fix the baffle indicator case.

5

Parts  List  of   Pump  Assembly

| Part No. | Description | Q’ty | Part No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 122H 123 124 125 126 127A 127B 127C 127D 128 129 130 131 132 133 134 135 | Steel ball Rod Base Steel roller Bushing Pin Shaft Retaining ring Axle Screw Washer Spring Pressure rod Steel ball Pressure valve body Split ring O-ring Washer Steel needle Bushing Pin Pump body Dust cover Bearing Steering wheel axle Bearing Steering wheel, Nylon Steering wheel, Polyurethane Steering wheel, Poly/Nylon Steering wheel, Rubber Retaining ring Steel ball Discharge valve body Spring O-ring Discharge valve shaft Valve taper core Spring | 1 1 1 1 1 1 2 1 1 1 1 1 1 1 1 1 2 2 1 2 2 1 1 1 1 4 2 2 2 2 2 1 1 1 1 1 1 1 | 136 137 138 139H 140H 141 142 143 144 145 146 147 148 149 150 151 152 153 154 155 156 157 157-1 158H 159H 160H 161H 162H 163H 164H 165H 166 167 168 169 170 171 | Pressure regulating screw O-ring Screw Crank link Setting screw Nut Parallel pin Retaining cover Spring cover Spring Pump rod Dust proof ring Pump cylinder Seal ring Nylon bushing Red copper washer Retaining ring Rhombus plate Pin Dowel pin Dust proof ring O-ring O-ring O-ring Cylinder Seal ring O-ring Filler plug Reservoir cover Screw Reservoir Retainer Retainer Retainer O-ring Retainer Dust cover Bearing Cover | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 2 2 1 1 1 1 1 1 1 1 1 2 1 3 1 1 1 1 2 |

# Parts  List  of  Handle

| Part No. | Description | Q’ty | Part No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| H101 H102 H103 H104 H105 H106 | Handle Spring pin Spring leaf Spring pin Spring pin Control lever | 1 1 1 2 1 1 | H107 H108 H109 H110 H111 H112 | Rod and chain Rubber cushion Screw Spring washer Nylon roller Spring pin | 1 1 3 3 1 1 |

## Parts  List  of  Frame

| Part No. | Description | Q’ty | Part No. | Description | Q’ty |
| --- | --- | --- | --- | --- | --- |
| F301 F302 F303 F304 F305A F306 F307 F308 F309 F310 F311 F312 F313 F314 F315 F316 F317 F318 F319 F320S F320L F321 F322 F323 F324 | Signal wire Screw Cover plate Screw Analog junction box Rubber Rubber Indicator case Knurled screw Indicator Bolt Washer Washer Spring washer Nut Bolt Wire clip Screw Fix screw Cover plate assembly (555mm) Cover plate assembly (690mm) Convex spherical washer Concave spherical washer Nut Set screw | 1 4 1 8 1 1 1 1 2 1 1 1 5 5 1 4 2 4 4 1 1 4 4 4 4 | F325 F326B F327S F327L F328 F329 F330 F101 F102 F103 F104 F105 F112 F113 F114 F115 F116B F117B F118 F119 F120 F121 F122 F123 F124 F126 | Bolt Load cell Frame (555mm) Frame (690mm) Pull rod Battery of indicator Charger of indicator Torsion tube assembly Bushing Hexagon socket screw Spring pin Torsion tube shaft Spring pin H-link Load roller axle Bearing Poly load roller, tandem type Poly load roller, single type Axle Roller Wheel frame H-link axle Pull rod axle Nut Spring washer Eccentric pin | 8 4 1 1 2 2 1 1 4 1 1 1 8/4* 2 4 8/4* 4 2 2 2 2 2 2 2 2 2 |

Note*: Quantity for tandem roller is 8, for single roller is 4.

Assembly  list

# Assembly          Description

AH                          Pump unit

B                           Lowering valve ass’y

CH                          Lowering screw ass’y

D                           Hydraulic valve ass’y

E                           Handle seat ass’y

F2                          Polyurethane steering wheel ass’y

G                           Handle ass’y

H1B                        Polyurethane load roller ass’y (tandem type)

H2B                        Polyurethane load roller (single type)

I2                          Tandem Polyurethane load roller system ass’y

L                           Rhombus plate ass’y

M                           Spring cover ass’y

N                           Pump piston ass’y

W                          Safety valve ass’y

SH                         *Seal kit

*Note: Seal kit include following parts: 111, 117, 118, 132, 137, 147, 149, 151,

156H, 157, 158H, 160H, 161H.

9. Wiring diagram of scale, junction box, sensor

### Note: Adjust corresponding relation

R12   Adjust Sensor 1

R4    Adjust Sensor 2

R16   Adjust Sensor 3

R8    Adjust Sensor 4

10. CHARGING

There is a charger as an accessory in the hand pallet truck with scale. When the indicator shows the battery need to be charged, first turn off the indicator, and then insert charging plug from the jack of indicator case (F308) one side, and connect the other side to AC supply. Now the charger is in the normal state of charging. There are two LBDs on the charger. The red LBD is pilot lamp of power signal and the green one is pilot lamp of charging signal. They are shining continually while the battery begins to be charged. When the battery has been to be charged enough, the charge cycle is complete, and the green LBD will go out. The charger has function of self-stopping charging.

11. TROUBLE SHOOTING OF WEIGHING UNIT

| NO | TROUBLE | CAUSE | SHOOTING |
| --- | --- | --- | --- |
| 1 | Data drift | -Fasterner or end of a thread in junction box is loosen or dropped. | -Check the connection in junction box after confirming safe. |
| 2 | Indicator can’t be turned on. | -Battery voltage is not enough. -Battery life is complete. -Charging jack is damaged. | -Charging -Replace rechargeable battery with new ones. -Replace charging jack. |
| 3 | Battery can’t be charged. | -Battery is damaged. -Charger is damaged. | -Replace rechargeable battery with new ones. -Check charger output voltage (17V~18V), replace charger with new ones. |
| 4 | While turning on scale, it display EEE | -Load on the fork. | -Move the load, and then turn on the scale. |
| 5 | While turning on scale, it display -EEE | -Connection between sensor and junction box is loosen or dropped. -Sensor is damaged. | -Check the connection between sensor and junction box. -Replace sensor with new ones. |